## Slide 1: Effective IDDQ Testing method to identify the fault in Low-Voltage CMOS Circuits
ECE 7502 Project Final Presentation
W.P Manula Pathirana
21st April 2015

## Slide 2
Requirements
Specification
Architecture
Logic / Circuits
Physical Design
Fabrication
Manufacturing Test
Packaging Test
PCB Test
System Test
PCB Architecture
PCB Circuits
PCB Physical Design
PCB Fabrication
Design and Test Development
Customer
Validate
Verify
Verify
Test
Test

## Slide 3: What is IDDQ testing?
IDDQ testing is simple method to identify the defects on IC based on the steady state power-supply current.
IDDQ(Measured)>IDDQ(Th) Defective
IDDQ flowing through inverter with and without defect[1]

## Slide 4: Problem statement
For new Technologies (Deep submicron levels)
Low threshold Transistors
Higher Leakage
IDDQ(Fault Free)≈IDDQ(Defective)
Test escapes and yield loss
A-test escapes
B-yield loss
Earlier Technologies[1]
Deep submicron Technologies[1]
[1]S. Sabade and D. M. Walker, “I DDX-based test methods: A survey,” ACM Trans. Des. Autom. Electron. Syst. TODAES, vol. 9, no. 2, pp. 159–198, 2004.

## Slide 5: Proposed Method
IDDQ versus Temperature[2]
ΔIDDQ(Faulty)<<IDDQ(Defect free)
Low temperature measurement is undesirable in production due to high cost
[2]A. Kaltchenko and O. Semenov, “Temperature dependence of IDDQ distribution: application for thermal delta IDDQ testing,” IET Circuits, Devices & Systems, vol. 1, no. 6, p. 509, 2007.

## Slide 6: Proposed Method
Expected out come
ΔIDDQ(Faulty)>> ∆IDDQ(Defect free)

## Slide 7: Proposed method
Estimate IDDQ distribution at V1 for an inverter
Estimate IDDQ distribution at V2 for an inverter
V2 >> V1
Estimate IDDQ distribution with artificially introduced faults at V1 and V2 for a simple inverter.
Each resistive path is injected with a resistor to the circuit under test
    Intragate shorts(happen within a CMOS gate)
Determine the V1,V2 and faults resistor values
Extend the proposed method from inverter to 1-bit adder
Explore the dependency of voltage delta IDDQ testing method on input logic using 1-bit adder
Extend the proposed method to 100-bit adder circuit.

## Slide 8: Result
Fault can only be identified with current monitoring techniques
Fault resistance value can be chosen as 5 kΩ
The inverter Wp/Wn ratio is 432µm/236µm

## Slide 9: Result
Monte Carlo simulation on inverter at different voltages
Test escape
Yield loss
Ith
Ith
Ith
Ith

## Slide 10: Result(voltage delta IDDQ testing)
The proposed method uses two samples.
A lot –Faulty circuit (Inverter with source drain short (Fault strength is 5kΩ)
B lot –Fault Free circuit
Monte Carlo simulation on Faulty Circuit at 0.1 V, 0.2 V and 0.25 V

## Slide 11: Result(voltage delta IDDQ testing)
The proposed method uses two samples.
A lot –Faulty circuit (Inverter with source drain short (Fault strength is 5kΩ)
B lot –Fault Free circuit
Monte Carlo simulation on Faulty Free Circuit at 0.1 V, 0.2 V and 0.25 V

## Slide 12: Result(voltage delta IDDQ testing vs. Thermal delta IDDQ)
No overlapping
Illustration of voltage delta IDDQ testing
Illustration of temperature delta IDDQ testing

## Slide 13: Result(voltage delta IDDQ testing)(1-bit adder)
Fault free circuit
Faulty circuit

## Slide 14: Result(voltage delta IDDQ testing)(1-bit adder)(A=B=Cin= 1)

## Slide 15: Result(voltage delta IDDQ testing)(1-bit adder)(A=B=0,Cin= 1)

## Slide 16: Result(voltage delta IDDQ testing)(1-bit adder)(A=Cin= 1,B=0)

## Slide 17: Result(voltage delta IDDQ testing)(1-bit adder)(A=0,B=Cin= 1)
Still ∆IDDQFaulty>> ∆IDDQFaultFree where ∆IDDQFaulty=1.3x10-6 A and ∆IDDQFaultFree = 5x10-7 A

## Slide 18: Result(voltage delta IDDQ testing)(100-bit adder) )(A=B=Cin= 1)

## Slide 19: Conclusion
Voltage delta IDDQ testing method is introduced.
The method is implemented on inverter,1-bit adder and 100-bit adder circuit.
By looking at ∆IDDQ on different voltage defected chip can be identified.(Usually ∆IDDQFaulty>> ∆IDDQFaultFree)

## Slide 20: References
[1] . S. Sabade and D. M. Walker, “I DDX-based test methods: A survey,” ACM Trans. Des. Autom. Electron. Syst. TODAES, vol. 9, no. 2, pp. 159–198, 2004.
[2]. A. Kaltchenko and O. Semenov, “Temperature dependence of IDDQ distribution: application for thermal delta IDDQ testing,” IET Circuits, Devices & Systems, vol. 1, no. 6, p. 509, 2007.
[3]. A. Abdollahi, F. Fallah, and M. Pedram, “Leakage current reduction in CMOS VLSI circuits by input vector control,” IEEE Transactions on Very Large Scale Integration (VLSI) Systems, vol. 12, no. 2, pp. 140–154, Feb. 2004.
[4]. Z. Chen, L. Wei, and K. Roy, “On effective I/sub DDQ/testing of low-voltage CMOS circuits using leakage control techniques,” Very Large Scale Integration (VLSI) Systems, IEEE Transactions on, vol. 9, no. 5, pp. 718–725, 2001.
[5].M. Karmani, C. Khedhiri, and B. Hamdi, “Design and test challenges in Nano-scale analog and mixed CMOS technology,” International Journal of VLSI design & Communication Systems (VLSICS) Vol, vol. 2, 2011.